## Slide 1
Omar Aziz, Noah Bolzoni, Brandon Castro,
Anthony Lucero, Sean Maggio, Marcin Wisniowski
Advised by: Professor Connington
October 10th, 2019
Phase 1 Presentation
Senior Design
Autonomous Subway Inspection Vehicle

## Slide 2: Outline
Background
Project Statement & Issues
Design
Concept Selection
Project Plan
Moving Forward
State-of-the-Art Technology & Needs
Technical Analysis
Problem
Notes: Marcin

## Slide 3
Background
Notes: Marcin

## Slide 4: Background
Manhattan subway service growth compared to ridership growth
(MTA, 2016)
5.7 million ride subway everyday
Subway system plagued by issues related to track defects
Problem
Notes: Marcin

## Slide 5: Background
Motivation
  Reactive inspection & maintenance cause high costs
  Too many delays from undiscovered defects
  Stagnant growth due to focus on keeping service running
Project Statement
Notes: Marcin

## Slide 6: Background
Autonomous Subway Inspection Vehicle Concept
Goals
  Autonomous system to collect key track data
    Detect defects more frequently by using multiple units
  Reduce costs & delays
  Minimize impact on service
  Increase growth & efficiency
Project Statement
Notes: Marcin

## Slide 7: Background
Project Statement
Major Issues
  Lack of publicly available specs
  Finding track that can be used for testing
  Cooperation with MTA/PATH
Notes: Marcin

## Slide 8: Background
MTA Track Geometry Car
(Bejarano, 2012)
Manual inspections
  Track geometry cars
    Large, expensive
  Visual inspection
    On foot, slow
Current Solution
Notes: Brandon

## Slide 9: Background
MTA Track Geometry Car
(MTA, 2015)
State-of-the Art Technology - MTA Track Geometry Cars
  Only 4 in service
  Up to $2.5 million each
  Manned by crew of 6+
  Inspect over 670 miles
  Full coverage only 6 times per year
Notes: Brandon

## Slide 10: Background
Sensing Equipment
(MTA, 2012)
State-of-the Art Technology - MTA Track Geometry Cars
  High-tech sensors
    Electro-mechanical
    Inertial
    Laser
  Comprehensive analysis
Notes: Brandon

## Slide 11: Background
UCF Mobile Railroad Cart
(University of Central Florida + FDOT, 2010)
  Research project
  Lasers, cameras to detect defects
  Machine learning & computer vision
    Inconsistent results
State-of-the Art Technology – Central Florida Hi-Rail Truck Cameras
Notes: Brandon

## Slide 12: Background
MTA Subway Delays
(New York Magazine, 2016)
Societal Needs
  Commuters need efficiency & safety
  Fewer delays & inconveniences
  Increased service
Needs
Notes: Brandon

## Slide 13: Background
Customer Needs
  Cost-effective solution
  Reliable measurements at higher frequency
  Save space & time
  Increase efficiency
  Increase revenue
Needs
MTA & Path Trains
Notes: Brandon

## Slide 14
Concept Selection
Notes: Sean

## Slide 15: Concept Selection
Initial Concept Sketches
Autonomous
(Self-propelled)
Mounted
Pulled/Pushed Cart
Stationary Sensors
Notes: Sean

## Slide 16: Concept Selection
Method Selection Matrix
Selection Criteria | Autonomous | Car-Mounted | Car-Dragged/ Pulled | Stationary
Requires System Modification | + | 0 | 0 | 0
Ease of Use | 0 | + | 0 | +
Installation | + | - | 0 | -
Impact on Operations | 0 | + | - | +
Low Cost | + | + | + | -
Moving Parts | - | + | - | +
Unique | + | - | + | 0
Net | 3 | 2 | 0 | 1
Rank | 1 | 2 | 4 | 3
Continue? | Yes | Yes | No | No
Notes: Sean

## Slide 17: Concept Selection
Method Selection Matrix
Design |  | Autonomous |  | Car-Mounted | 
Selection Criteria | Weight | Rating | Weighted Score | Rating | Weighted Score
Impact on Operations | 25.00% | 3 | 0.75 | 5 | 1.25
Low Cost | 20.00% | 4 | 0.8 | 3 | 0.6
Requires System Modification | 15.00% | 5 | 0.75 | 3 | 0.45
Ease of Use | 15.00% | 3 | 0.45 | 3 | 0.45
Installation | 15.00% | 5 | 0.75 | 1 | 0.15
Moving Parts | 5.00% | 2 | 0.1 | 4 | 0.2
Unique | 5.00% | 5 | 0.25 | 1 | 0.05
Total Score |  | 3.85 |  | 3.15 | 
Rank |  | 1 |  | 2 | 
Continue? |  | Yes |  | No | 
Notes: Sean

## Slide 18: Concept Selection
Refining
Autonomous Vehicle
Measurement
What to Measure
How to Measure
Train Evasion
Trigger
Mechanism
Notes: Sean

## Slide 19: Concept Selection
What to Measure – Definite Values
Track Gauge
Rail Profile
Worn
New
Notes: Sean

## Slide 20: Concept Selection
What to Measure – Possible Values
Crosslevel
Curvature
Level Ground
Notes: Sean

## Slide 21: Concept Selection
How to Measure – Gauge
Chassis to Rail
Sensor to Sensor
Inductive
Laser/Photoelectric
Capacitive
LVIT or LVDT
Linear Variable Inductance Transducer
Linear Variable Differential Transformer
Notes: Sean

## Slide 22: Concept Selection
How to Measure – Profile
Multiple points using Inductive, Capacitive, Photoelectric, or LVIT/LVDT
2D profile Laser Scanner
Camera + Machine Learning
Notes: Sean

## Slide 23: Concept Selection
How to Measure – Crosslevel & Curvature
Sensor banks extend beyond chassis
Data from each bank compared
Similar sensors to gauge setup
OR:
Angular acceleration data from accelerometer
Curvature
Crosslevel
Gyroscope and accelerometer data
Notes: Sean

## Slide 24: Concept Selection
Train Evasion - Trigger
External Detection
Onboard Detection
Notes: Omar

## Slide 25: Concept Selection
Train Evasion - Mechanism
Concept 1: Folding Wheels
Concept 2: Retracting Wheels
Front View - Folded
Side View -Folded
Side View - Unfolded
Front View - Unfolded
Notes: Omar

## Slide 26: Concept Selection
Train Evasion - Mechanism
Concept 2a: Rack-and-Pinion
Top View - Extended
Top View - Retracted
Isometric View
Notes: Omar

## Slide 27: Concept Selection
Train Evasion - Mechanism
Concept 2b: Single Actuator (Mechanically Linked)
Top View - Extended
Top View - Retracted
Isometric View
Notes: Omar

## Slide 28: Concept Selection
Train Evasion - Mechanism
Concept 2b: Dual Actuator (Directly Driven)
Top View - Extended
Top View - Retracted
Isometric View
Notes: Omar

## Slide 29: Concept Selection
Train Evasion - Mechanism
Dual Actuator Concept Simulation
Notes: Omar

## Slide 30: Concept Selection
Train Evasion - Mechanism
Dual Actuator Concept Simulation
Notes: Omar

## Slide 31: Technical Analysis
Motor Torque, Power, & Speed comparison
(MIT Center for Innovation in Product Development, 1999)
Electronics
  Microcontroller, sensors, etc.
  DC Motors
Power Calculations
Notes: Noah

## Slide 32: Technical Analysis
Train Braking System
(Quora, 2018)
Kinetic & potential energy
Max braking force
Braking distance
Braking Forces
Notes: Noah

## Slide 33: Technical Analysis
Track gauge
Other relations to explore
  Gyroscope output angle
    Measure crosslevel, alignment
  Correcting distance measurements for wheel slip
Sensor Calculations
Notes: Noah

## Slide 34
Moving Forward
Notes: Anthony

## Slide 35: Project Plan
Full CAD model
Alpha prototype
Testing location
Functionality testing
Defect testing
Analysis and recommendation
Deliverables
Notes: Anthony

## Slide 36: Project Plan
Preliminary Budget
Item: | Allocation:
Sensors | $200
3D Printed Parts | $150
Housing | $150
Drivetrain Parts | $200
Total: | $700
Notes: Anthony

## Slide 37: Project Plan
Condensed Timeline
Notes: Anthony

## Slide 38: Recap
Autonomous system to collect key track data
  Measurement & evasion
    Gauge, profile, level
    Retract from track
Reduce costs, delays
Summary
Notes: Anthony
*****RETURN TO THIS SLIDE WHEN PRESENTATION IS OVER********

## Slide 39
Appendix

## Slide 40: Appendix
Full Gantt Chart

## Slide 41: Appendix
Gantt Chart Sec. 1

## Slide 42: Appendix
Gantt Chart Sec. 2

## Slide 43: Appendix
Gantt Chart Sec. 3

## Slide 44: Appendix
“Graphic list of track gauges”, Track Gauge, Wikipedia
  (By Rail_gauge.svg: http://commons.wikimedia.org/wiki/User:IRTC1015derivative work: HTML2011 (talk) - Rail_gauge.svg, Public Domain, https://commons.wikimedia.org/w/index.php?curid=17669390)
“Two commonly used rail profiles: a heavily worn 50-kg/m profile and a new 60-kg/m profile”, Rail Profile, Wikipedia
  (By MADe - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=3440945)
Linear Rod with Return Spring, Novotecknik, website
  (https://www.novotechnik.com/Linear-Rod-With-Return-Spring/linear-rod-ret-spr.html)
“Inductive sensors (eddy current) for displacement, distance and position”, Sensors for Displacement, Distance and Position, Micro-Epsilon, website
  (https://www.micro-epsilon.com/displacement-position-sensors/)
“Capacitive displacement sensors and measurement systems”, Sensors for Displacement, Distance and Position, Micro-Epsilon, website
  (https://www.micro-epsilon.com/displacement-position-sensors/)
References

## Slide 45: Appendix
“Laser sensors for displacement, distance and position”, Sensors for Displacement, Distance and Position, Micro-Epsilon, website
  (https://www.micro-epsilon.com/displacement-position-sensors/)
“The measurement of crosslevel between two rails”, Track Geometry, Wikipedia
  (By Z22 - Own work, CC0, https://commons.wikimedia.org/w/index.php?curid=22764594)
Train Track Clipart, Clip Art Mag, website
  (http://clipartmag.com/train-track-clipart)
“Inductive Sensing”, Proximity Sensors Compared: Inductive, Capacitive, Photoelectric, and Ultrasonic, MachineDesign, website
  (https://www.machinedesign.com/sensors/proximity-sensors-compared-inductive-capacitive-photoelectric-and-ultrasonic#menu)
“Capacitive Sensing”, Proximity Sensors Compared: Inductive, Capacitive, Photoelectric, and Ultrasonic, MachineDesign, website
  (https://www.machinedesign.com/sensors/proximity-sensors-compared-inductive-capacitive-photoelectric-and-ultrasonic#menu)
“Photoelectric/Ultrasonic Sensing Setups”, Proximity Sensors Compared: Inductive, Capacitive, Photoelectric, and Ultrasonic, MachineDesign, website
  (https://www.machinedesign.com/sensors/proximity-sensors-compared-inductive-capacitive-photoelectric-and-ultrasonic#menu)
References