## Slide 1
Omar Aziz, Noah Bolzoni, Brandon Castro,
Anthony Lucero, Sean Maggio, Marcin Wisniowski
Advised by: Professor Connington
November 14th, 2019
Phase 2 Presentation
Senior Design
Autonomous Subway Inspection Vehicle

## Slide 2: Outline
Background
Project Statement
System Design
Sensors and Control
Project Plan
Moving Forward
Problem
Feedback
Alpha Prototype
Technical Analysis
Deliverables
Notes: Marcin

## Slide 3
Background
Notes: Marcin

## Slide 4: Background
5.7 million ride subway everyday
  Too many delays
Track Geometry Cars are too few and too expensive
  Reactive inspection & maintenance cause high costs
Problem
MTA Track Geometry Car
(Bejarano, 2012)
Notes: Marcin

## Slide 5: Background
Autonomous Subway Inspection Vehicle Concept
Autonomous, independent vehicle to collect key track data
Detect defects more frequently
Reduce costs & delays
Minimize impact on service
Increase subway growth & efficiency
Project Statement
Notes: Marcin

## Slide 6: Background
“Projections for device and sensors?” “Harsh environment.”
  Micro-Epsilon Sensor IP 67 (dust tight, submerged 30 min 1 meter of water)
“Locomotion discussion not present”
  Battery powered for flexible use
  Electric motors
Feedback
Notes: Marcin

## Slide 7: Background
“Too many parameters, will be overwhelmed”
  Focus on track gauge
  Velocity closed loop control and measurement sync.
Feedback
Notes: Marcin

## Slide 8: Background
“Too many actuators,” “Wheel retraction mechanism confusing/appears too complex”
  Simplest design will need more actuators for stability
    4 independently actuated (linear) legs most stable for uneven ground
    2 linear actuators for wheel retraction to be able to attach directly without more complex mechanisms (linkages)
      Also increases retraction range
Feedback
Notes: Brandon

## Slide 9: Background
“Too many actuators,” “Wheel retraction mechanism confusing/appears too complex”
  2 horizontal linear actuators will allow system to adapt to different track gauges and systems, increasing market value
  Retraction mechanism not possible with a fixed axle
  1 motor per wheel is needed to avoid using more complex transmission mechanisms to transmit power to multiple wheels from fewer motors
Feedback
Notes: Brandon

## Slide 10: Background
“Recommended two axle vehicle, third axle with passive measurement systems. Should not be allowed on active tracks, should attach to trains”
  Project is to create an autonomous vehicle, not a sensor box
    The vehicle is a mechanical engineering project, an attached box is not
  Sensor boxes that attach to trains exist, but are expensive due to distance from track and must be retrofitted
Feedback
Notes: Brandon

## Slide 11: Background
“For safety reasons, inspection vehicle should not be allowed to move alone on active tracks”
  Team understands the safety issues, effort is being put in the evasion mechanism to ensure max reliability
  Positive Train Control System and Communications Based Train Control are new systems in place today that let operators know exactly where trains are
Feedback
Notes: Brandon

## Slide 12: Background
“For safety reasons, inspection vehicle should not be allowed to move alone on active tracks”
  Vehicle can be connected to the communications network for trains so that it’s location can be known
  Train locations can be relayed to the vehicle so it can get off the tracks while the train passes
  Vehicle will be designed to function separately and detect trains regardless of the communication system
Feedback
Notes: Brandon

## Slide 13: Background
“Technical analysis too simple, need statistical analysis of sensors”
  More understanding of sensors and vehicle design was needed before going in depth with analysis
  Micro-Epsilon sensors are high precision
    Low repeatability error
    Micrometer resolution
    Error margin doubles with two sensors, but still extremely small
Feedback
Notes: Brandon

## Slide 14
System Design
Notes: Sean

## Slide 15: System Design
Focus on measuring track gauge
  MTA regards as most important
  FRA: 15-20% of track issues from wide gauge
  Use distance sensors to measure
Inertial data may also need to be collected
  Accelerometer and gyroscope
Measurement Control System & Velocity Control System (Closed Loop)
Sensors and Control
Notes: Sean

## Slide 16: System Design
Compared distance sensor types during Phase 1
  Inductive
  Capacitive
  Ultrasonic
  Laser
Sensors and Control
Notes: Sean

## Slide 17: System Design
Inductive Distance Sensor
  Hard to measure thick metal
  High temperature sensitivity
  Not reliable above 3 deg. Tilt
  Requires large targets relative to sensor, especially over longer range
  Not viable
Sensors and Control
Notes: Sean

## Slide 18: System Design
Capacitive Distance Sensor
  Also affected by tilt
    0.5-0.8% of full scale output (FSO) at 1 deg. tilt
  Requires large targets relative to sensor
  Not viable
Sensors and Control
Notes: Sean

## Slide 19: System Design
Ultrasonic Distance Sensor
  Up to 45 deg. tilt
  Requires wide targets
  Accuracy dependent on constant air temperature
  Not viable
Sensors and Control
Notes: Sean

## Slide 20: System Design
IR Time-of-Flight (TOF) Distance Sensor
  Inexpensive
  Sensitive to ambient light
  IR beam widens over longer ranges
  Most have poor resolution (~1cm)
  Viable for Alpha Prototype
Sensors and Control
Notes: Sean

## Slide 21: System Design
IR Time-of-Flight (TOF) Distance Sensor
  Purchased VL6180X for Alpha Prototype
    $8.50
  Made for lower ranges
    Accuracy up to 1mm at 10cm range
  Up to 400kHz communication
  Easy to interface with microcontrollers, I²C
  Cheap, accurate alternative to lasers
Sensors and Control
Notes: Sean

## Slide 22: System Design
Laser Distance Sensors
  Single point, very accurate
  Micro-Epsilon sensors
    Up to 30 deg. tilt with <1% error
    IP67 Rating
Sensors and Control
Notes: Sean

## Slide 23: System Design
Control
  Velocity (closed loop)
    Incremental motor encoders
  Measurement control systems
    Arduino and I²C for high frequency data collection
  Master and slave setup for subsystem control
    Raspberry Pi as master for computation tasks
    Arduino as slaves for control of a specific subsystem
Sensors and Control
Notes: Sean

## Slide 24: System Design
Data Collection
  Assuming 25 mph and 1.5kHz max freq. (laser)
    Measurement every ~8 mm
    1 byte per data point : 5000+ miles per GB
Sensors and Control
Notes: Sean

## Slide 25: System Design
Technical Analysis
Forces
FR → Rolling Resistance
FD → Air Drag
FM → Motors
Notes: Noah

## Slide 26: System Design
Technical Analysis – Motor Power
Velocity: 25mph
Notes: Noah

## Slide 27: System Design
Technical Analysis – Motor Selection
Single motor (Alpha)
  400W DC brushed motor
  Rated 22 Amp
  2 axle, front powered through chain/sprocket
Four motors (Beta)
  4x 100W DC brushed motor
  Wheel retraction mechanism does not allow for axles
  Better traction, dynamic/independent control for stability
400W Scooter Motor
100W Scooter Motor
Notes: Noah

## Slide 28: System Design
Technical Analysis – Braking Force
Work-Energy Equation:
Linear Kinetic Energy
Rotational Kinetic Energy
Potential Energy
Braking Work
Resistance Work
Notes: Noah

## Slide 29: System Design
Technical Analysis – Braking Force
Stop within 50 meters from 25mph at 50mm/m downhill grade, no resistance (Worst-case scenario)
Total Braking Force
Notes: Noah

## Slide 30: System Design
Technical Analysis – Braking Force
Assuming 4 brakes (1 per wheel) for the beta prototype
Braking Force per Wheel
1 brake for the alpha prototype
  184.7 N braking force
Notes: Noah

## Slide 31: System Design
Technical Analysis – Braking Force
Servo motor (high torque) to pull on brake cable
  20kg-cm
  Arm length of 25mm
    Output force of 78N
For beta prototype
  78N per wheel >> 46.2N required
For alpha prototype
  78N < 184.7N required
    Reduce through use of pulleys or use higher torque servo
Notes: Noah

## Slide 32: System Design
Technical Analysis – Battery Selection
Assuming 15-mile inspection at 25 mph
  36-minute run time
  Motors are most power consuming (by large margin)
Notes: Noah

## Slide 33: System Design
Technical Analysis – Battery Selection
6.48Ah  7Ah
Sealed Lead Acid
  Safer than Lithium-ion, no fires
2x 12V 7Ah batteries in series
  24V 7Ah
  24V needed for motors
Notes: Noah

## Slide 34: System Design
Alpha Prototype – Isometric View
Notes: Omar

## Slide 35: System Design
Alpha Prototype – Top View
Motor
Batteries
Bearing
Axle
Wheel
Disk Brake
Sprocket
Chain
Sensor Mount
Notes: Omar

## Slide 36: System Design
Alpha Prototype – Close Up
Motor
Batteries
Bearing
Axle
Wheel
Disk Brake
Sprocket
Chain
Sensor Mount
Notes: Omar

## Slide 37: System Design
Alpha Prototype – Front View
Notes: Omar

## Slide 38: System Design
Alpha Prototype – Sensor Mount
Notes: Omar

## Slide 39: System Design
Alpha Prototype – Axle Analysis
Axle : Stainless Steel 304 5/8” Rod
Deformation analysis assuming 40kg vehicle (100N per bearing)
100N (Bearing)
100N (Bearing)
Wheel (fixed)
Wheel (fixed)
Max Deformation: ~5mm at center (Acceptable)
Notes: Omar

## Slide 40: System Design
Alpha Prototype – Progress
Notes: Omar

## Slide 41: System Design
Alpha Prototype – Progress
Motor
Motor Driver
Power Supply
Arduino Nano
Potentiometer
Notes: Omar

## Slide 42: System Design
Alpha Prototype – Progress
Motor
Motor Driver
Power Supply
Arduino Nano
Potentiometer
12V 7Ah SLA Batteries
12V 1.2A Phased Charger
Gyro + Accel + Compass IMU
Notes: Omar

## Slide 43: System Design
Alpha Prototype – Progress
Motor
Motor Driver
Power Supply
Arduino Nano
Potentiometer
VL6180X ToF Distance Sensor
SS 304 5/8” Rod
5/8” Pillow Block Bearings
Notes: Omar

## Slide 44
Moving Forward
Notes: Anthony

## Slide 45: Moving Forward
Deliverables
Alpha prototype parts
Track gauge analysis code
Alpha prototype
Testing location
Testing and analysis
Forward recommendation
Notes: Anthony

## Slide 46: Moving Forward
Project Plan - Budget
Purchased Sensors | 
Item: | Price:
Laser Sensors | Donation from Micro-Epsilon
Gyro + Accelerometer Unit | $15.95
IR Time-of-Flight Sensor (x3) | $25.47
Total: | $41.42
Notes: Anthony

## Slide 47: Moving Forward
Project Plan - Budget
Purchased Parts | 
Item: | Price:
SS 304 5/8” Rod (x2) | $26.50
Pillow Block Bearings (x4) | $22.58
12V 7AH SLA Battery (x2) | $34.40
12V Battery Charger | $9.99
Total: | $93.47
Remaining Budget: $565
Notes: Anthony

## Slide 48: Moving Forward
Project Plan - Timeline
Notes: Anthony

## Slide 49: Moving Forward
Project Plan - Timeline
Notes: Anthony

## Slide 50: Moving Forward
Project Plan - Timeline
Phase 4
  Test Alpha Prototype
    Date: 1/21/2020
Phase 5
  Assemble Beta Prototype
    Date: TBD March/April
  Test Beta Prototype
    Date: TBD March/April
Notes: Anthony

## Slide 51
Appendix
Notes: Anthony

## Slide 52: Appendix
Full Gantt Chart
Notes: Anthony

## Slide 53: Appendix
References
TGC - https://www.youtube.com/watch?v=gE0F4aDhwU8
Opto sensor - catalog
AlveyTech 24 Volt 100 Watt Electric Motor for Razor E100, E124, E150, and E175 - https://www.amazon.com/AlveyTech-Volt-Electric-Motor-Razor/dp/B01MTDKNF8
ANNIMOS 20KG Digital Servo High Torque Full Metal Gear Waterproof for RC Model DIY, DS3218MG,Control Angle 270° - https://www.amazon.com/ANNIMOS-Digital-Waterproof-DS3218MG-Control/dp/B076CNKQX4
Powersonic PS1270F1 Replacement Rhino Battery - 2 Pack - https://www.amazon.com/Powersonic-PS1270F1-Replacement-Rhino-Battery/dp/B008AYQ624
Notes: Anthony