## Slide 1: Autonomous Subway Inspection Vehicle
Phase
4
Senior Design
Omar Aziz, Noah Bolzoni, Brandon Castro,
Anthony Lucero, Sean Maggio, Marcin Wisniowski
Advised By Professor Connington
February 27th, 2020

## Slide 2
Outline
Background
Technical Analysis
Engineering Design
Moving Forward
Alpha & Beta
Demo
4
3
2
1
A
B

## Slide 3
Background
1

## Slide 4
Background
The New York Subway has been around since 1904
5.7 million ride subway everyday
Daily wear and weather elements affect the rails
  Weekly inspections needed for mainline track
  Reactive inspection and maintenance leads to high costs
2

## Slide 5
Project Overview
Cannot rebuild network, must maintain and slowly improve
In New York, geometry trains run non-stop with employees monitoring the rails but only fully inspect a few times per year
3

## Slide 6
Project Overview
Autonomous vehicle to collect key track data
More frequent, non-intrusive inspections
Increase subway revenue, efficiency, and safety
4

## Slide 7
Design Rationale
MTA capital plan includes hundreds of millions poured into CBTC, communication-based train control
  With this, trains can pinpoint exactly where other trains are, and autonomy can be achieved in the near future
5

## Slide 8
Design Rationale
A smaller and cheaper inspection vehicle has yet to ever be implemented and can prove to be beneficial for consistent measurement scenarios
6

## Slide 9
Technical Analysis
2

## Slide 10
Revised Motor Analysis
Acceleration from rest requires:
  High Torque
  High Current Draw
8

## Slide 11
Revised Motor Analysis
Target values were selected for normal operation and a “reduced” value for use when subject to a considerable gradient
Target | Alpha Prototype | Beta Prototype
Normal Operating Velocity | 5 mph | 10 mph
Normal Acceleration | 0.2 m/s2 | 0.2 m/s2
Reduced Velocity | 2.5 mph | 5 mph
Reduced Acceleration | 0.0667 m/s2 | 0.0667 m/s2
Gradient | 20 mm/m | 20 mm/m
9

## Slide 12
Revised Motor Analysis
Alpha
1x 400-Watt motor
Powering single axle
Rated at ~1 Nm torque
Max 22A
Beta
2x 150 Watt Motors
Powering two independent axles
Rated at 0.52 Nm torque
Max 9.6A
10

## Slide 13
Revised Motor Analysis
Calculations based on similar mechanical characteristics for both prototypes
Calculated Value | Alpha Prototype | Beta Prototype
Starting Torque Uphill | 1.039 Nm | 0.5196 Nm
Starting Torque on Level Track | 0.8082 Nm | 0.4041 Nm
Torque Uphill at Constant Speed | 0.8300 Nm | 0.4690 Nm
Torque on Level Track at Constant Speed | 0.2161 Nm | 0.3239 Nm
11

## Slide 14
Revised Motor Analysis
Current derived from motor torque voltage constant
Calculated Value | Alpha Prototype | Beta Prototype
Starting Current Uphill | 13.79 A | 8.734 A
Starting Current on Level Track | 11.17 A | 6.971 A
Current at Constant Speed | 11.42 A | 7.962 A
Current on Level Track at Constant Speed | 4.451 A | 5.746 A
12

## Slide 15
Measurement and Control
Outputs and functions:
  Data collection at fixed intervals (odometer)
  SD card write of measurements w/ time & location to CSV(Excel)
  Evasion mechanism with detection, retraction, extension
User inputs
  Speed and direction control
    Variable throttle
  Data collection on/off
  Evasion trigger (testing)
  Wireless Arduino - Arduino communication
    May first operate using extended wire connections
13

## Slide 16
Additional Functionality
Long range proximity sensors on front and rear
  Stop if object detected
  Movement away from approaching object
Evasion triggered by forward and rear proximity sensors
Three data collection modes
  Time interval
  Distance interval
  Instantaneous measurement (manual)
3D mapping of rails
  Calculate rails as series of coordinates using IMU and gauge
  MATLAB display, onboard or using saved coordinates
14

## Slide 17
Hardware
VL1680X IR ToF
minIMU v5
optoNCDT 1402
Adafruit DataLogger Shield
Arduino Mega
15

## Slide 18
Electrical System Architecture
16

## Slide 19
Electrical System Architecture
17

## Slide 20
System Integration
Test items separately
  Ex: learn to use RTC, then learn to use write to SD, then combine
Integrate individual items and functions in full software architecture
18

## Slide 21
Errors
19

## Slide 22
Engineering Design
3

## Slide 23
Alpha Prototype
20

## Slide 24
Fabrication
Lathe
Manually created features
  Bore holes, turning diameter, cut parts from each other
Set references to be used in programs
Wrote programs to create more complicated features multiple times
Used broaching tool and press to make keyways
21

## Slide 25
Fabrication
Milling Machine
Manually used machine to set references
Wrote a program to recreate the exact wheel part four times
22

## Slide 26
Testing
23

## Slide 28
Testing
25

## Slide 29
Testing
26

## Slide 30
Testing
27

## Slide 32
Beta Prototype
29

## Slide 33
Beta Prototype
30

## Slide 34
Beta Prototype
31

## Slide 35
Beta Prototype
32

## Slide 36
Beta Prototype
33

## Slide 37
Moving Forward
4

## Slide 38
Deliverables
Procure Remaining Beta Prototype Parts
Assemble Beta Prototype
Contact MTA for Testing Location
Testing and Analysis
Design Tweaking
35

## Slide 39
Budget
Sensors and Electronics | 
Item | Price
Light Sensors | Donation
Gyro, Accelerometer, and Compass | $15.95
Time-Of-Flight Sensor (x3) | $25.47
Adafruit DataLogger Arduino Shield + Button Battery + Stacking Headers | $27.49
Arduino Mega 2560 Microcontroller Rev3 | $40.10
M12 12-Pole Cables (x2) | $72.00
Total: | $181.01
36

## Slide 40
Budget
Drivetrain Parts | 
Item | Price
Rod (x2) | $26.50
Pillow Block Bearing (x4) | $22.58
12 V 7AH SLA Battery (x2) | $34.40
12 V Battery Charger | $9.99
Total | $93.47
Total Cost (Electrical + Mechanical): | $292.87
Remaining Budget: | $407.13
37

## Slide 41
Timeline
38

## Slide 42
Deliverables
Phase 5
Assemble Beta Prototype
  Date: March 23, 2020 - March 30, 2020
Procure Testing location w/ MTA
  Date: March 13, 2020
Test Beta Prototype
  Date: March 30, 2020 - April 8, 2020
39

## Slide 43
Appendix

## Slide 44
Gantt Chart

## Slide 45
Gantt Chart